## Slide 1: “This is Serious”
With thanks to UH for Original article on this
Topic (Valley Soaring, Out-of-the-Valley Newsletter)

## Slide 2: “This is serious”
This thought will jump into each pilots mind once in a while as a difficult situation becomes critical;
Each of us has a different threshold of alarm;
What we are talking about is “fine tuning that alarm system” so we are prepared to use it;
The level of discussion here is when we are looking to minimize probable damage to the sailplane or choosing to increase it to prevent injury or death;
Virtually all of the situations that apply to this category are related to the launch or landing phases;
We will examine some general guidelines and a few examples.

## Slide 3: Point 1: Where the sailplane lands is much less important than it landing at minimal speed under control

## Slide 4
A slow speed (near stall), wings level impact virtually anywhere is survivable provided you don’t run the nose into something. It is better to land in the trees at minimum speed than be out of control going into a small field;
If the tow-plane dies (rope break, etc.), a straight ahead landing into anything but a wall is survivable at minimum speed. Straight ahead into tall corn, bushes, whatever may damage the sailplane. A big old cartwheel or ground loop while turning definitely will, and may break your back or kill you;
In an off field landing, the approach that lets you land slowly is much more important than the surface. With a good approach, almost any field has an area good enough for minimal damage. Again we are talking about making the best of a bad situation we should have avoided. In any case the low energy landing, wings level, will reduce injury probability to a minimum, and fatality probability to almost none. This does not mean a slow pattern, but slow touchdown. Practice this until it is a habit.

## Slide 5: Point 2: Fly the sailplane first

## Slide 6
If the canopy comes open, fly the sailplane first and deal with the canopy later;
If a bee, snake, mouse, spider, whatever, shows up, fly the sailplane first. Getting bitten or stung is much less likely to be fatal than a crash.

## Slide 7: Point 3: If things seem to be getting out of hand, maybe they are.

## Slide 8
If the elevator doesn’t seem to be working on takeoff, release now! It only gets worse as speed and altitude, build up;
If an aileron or dive brake is disconnected, you should still have enough control to maintain a normal attitude. If it is a dive brake, you may need to partially or fully open the other one to compensate for the rolling moment. Don’t jump the gun on releasing from tow if you can maintain position;
If you get a severe pitch up on tow, don’t kill the tow pilot, release before you are totally out of control;
Practice bailout procedures till you can do them blind in the sailplane you are flying;
There has been much talk recently about crashworthiness of some sailplane. The important thing to remember is that virtually all accidents are survivable if you don’t bash the nose into the ground by stalling, diving or cartwheeling;
Each pilot must decide beforehand to release when the tow is getting out of hand while you can still retain control;

## Slide 9: Point 4: It’s better to have a low energy crash under control than a fatal almost save.

## Slide 10
It may sound like we are saying all accidents are OK to have;
Not true. It is however important to remember that many fatal accidents could have been prevented from being fatal by accepting the possibility of sailplane damage in order to have a low energy survivable accident.

## Slide 11: Things we can do to improve our chances in difficult situations.
Some of these will seem like common sense and some you probably have never considered:

## Slide 12: Mindset and Attitude
Avoiding Bad Situations
ADM

## Slide 13: Plan & Think Ahead
Think and fly to avoid getting into a bad situation in the first place.
Methodically envision what may happen ahead:
Always have:
    Two aerological plans: two cumulus, or cumulus + ridge;
    An escape to a landing: airport or landable fields;
Abide by these two: Don’t be complacent… just because you’ve gone past one or both of these tenants in the past and gotten away with it doesn’t mean it will work out next time.

## Slide 14: Equipment
To be prepared

## Slide 15: Parachutes
Know how to set up and use your parachute;
Make sure the harness and pads are correct for you and properly adjusted;
Practice and make second nature the procedures for getting out of the ship;
Eliminate things in the cockpit that would make egress more difficult;
Make sure the canopy jettison mechanism works to release properly and that it returns all the way to its home position on reassembly. You do it, your mechanic probably didn’t.

## Slide 16: Loose Objects
Before you put something in the “baggage compartment” behind you head, ask the following question: “Would I want this to be thrown at my head by a very strong man?”.
  If the answer is “no” either bolt it down (no bungee cords) or leave it out.
Shot bags and batteries loosely secured become lethal weapons in an accident. In 1986, a top ranking US national pilot was killed by a shot bag bungeed into the baggage compartment.

## Slide 17: ELT’s; PLB’s; Spot Trackers etc.
If you fly cross country, particularly over terrain with few landing options or that is sparsely populated (welcome to Vermont), an ELT is a good idea;
  If you still have an old 121 only ELT, consider updating to a 406 capable unit or adding a 406 PLB;
Also consider that an inexpensive hand-held radio might be more likely to be working after an accident than your normal installed radio;
You cannot rely upon having cell phone coverage when you land out in Vermont. Consider a satellite tracker such as a Spot, In-reach etc.

## Slide 18: Communication
If you are close to landing out, radio with a simple call e.g. “IC low near …………..if you don’t hear from me within 15 minutes expect a phone call”. If you are still in the air a little later simply update;
  This can speed up a retrieve and significantly increase your chances of getting help quickly in the event of an accident;
If it is late in the day or you haven’t spoken to anyone in an hour or more, another simple call that can set peoples mind at ease is “IC.. Still flying”
Keep in the glider at all times – Money, credit card, NESA cell phone list and your personal emergency information and contact. If you haven’t made up and ICE card – do so now!
  This is especially important if you have special medical needs such as allergies or sensitivities to particular medications etc.

## Slide 19: Simple Survival/Land-out Kit
Be prepared for a long wait for retrieve or rescue:
Simple first aid kit?
Space blanket?
Food?
A way to start a fire?
Whistle?
Warm attire if not flying wearing such;
Etc.

## Slide 20: Recipe for a Great Season:
Have fun,
Think safety, Fly safely,
Be prepared.